List of modifications of Version 3.3 of miniBackplane (SFP, 18 ports):

Schematics:
- Connector_GTX.SchDoc:
  - P/N of the J1 changed to QTS-048-02-L-LD-DP (8 mm height stack-up)
  - Pin-90 signal connected to FAN_BOX_EN
  - Pin-92 signal connected to FAN_PSU_EN
- Powe_Supply.SchDoc:
  - N/A
- I2C_Multiplexers.SchDoc:
  - Removed I2C Temperature Sensor TMP100 IC7 for sensing PCB Tª (placed close the PSU)
- TEST_USB.SchDoc:
  - Removed the two 1:2 multiplexer controlled by the FPGA.
  - Used two independent USB CP2101 chips and connectors for ARM and FPGA.
  - Resistors for pull-up and pull-down changed from 3K3 to 4K7.
- Connectors_GPIOs.SchDoc:
  - Cases of the DB9 and USB connectors tied to chassis.
  - P/N of the J2 changed to QTS-048-02-L-LD-DP (8 mm height stack-up)
  - Removed FAN_FPGA controller
  - FAN_BOX_EN and FAN_PSU_EN controlled by the FPGA in order to allow easy PWM implementation.
  - Added capacitors for filtering PWM output signals.
  - Removed tachometers fan signals.
  - Added general function push-button.
  - Added PMOS to allow switch on-off the +12V of the fans.
- WR_LINK.SchDoc:
  - N/A
- Main.SchDoc:
  - Removed Chassis connections
  - Added the I2C_Peripherals sheet:
    - Added I2C GPIO controller
    - Added push-button to select the ARM booting
    - Added a bi-colour red/green led for ARM error communication
    - Added a bi-colour red/green led for PSU OK/error
    - Added 4bit dip-switch to indicate the PCB version
    - Added the TMP100 I2C IC7 Tª sensor removed from I2C_Multiplexers.

PCB:
- PCB shape changed
- RS232 and USB Test connectors moved to the back panel of the switch.
- SFP case moved about 2,4mm inside PCB
- USB connectors moved to the PCB border
- Stack-up changed to 6 layers.
- Gigabit signals moved to internal routing layers.