The schematics changes performed on the V3.2 are the following:

1.- SCB_PLLs:
C165 footprint changed to 0402 in order to remove this component and reduce boom.
2.- Connectors:
CN1 Ethernet connector case connected to GND_SHIELD.
3.- CPU_100M_Ethernet:
- C206 changed from 470pF to 2,7nF in order to remove this component and reduce boom.
- Added R253 and R254 resistors (both 75R) between the Tr1 and C214.
- L10 is not mounted now. It connects GND_SHIELD and GND_ETH.
4.- QDRII_mem and QDRII_power:
All the components of the QDRII memories will be not mounted.