The detected errors and changes performed on the SCB Board (Schematics and routing) over the last version are:

Schematics:

1.- Connectors:
FPGA JTAG connector, TDI and TDO swapped.
FPGA JTAG Header changed to 0878321421 Molex.
P2 Header changed by a 2mm SMD version.
Added FPGA fan connector P9.
Changed USB schematics ports for CPU_USB harness.
2.- CPU_DDR2
Error in ARM EBI0 symbol. RAS and CAS pins are swapped.
Signals DDR_DQM0 and DDR_DQM1 to DDR are swapped.
Signals name updated by pin swapping in serial resistors.
3.- SMI_Link_7-12:
Swapped P/N lines in some differential pairs in order to fix error introduced by the pin swapping process during the PCB routing.
4.- uTCA_Tongue3:
Swapped P/N lines in some differential pairs in order to fix error introduced by the pin swapping process during the PCB routing.
5.- SCB_PLLs:
Added pull-down resistor to RESET and PD AD9516 pins. Both pins are connected together.
Added pull-resistor to EN pin of IC12 (clock driver). This pin is now controlled by FPGA.
This changes are for improving power consumption when both chips (IC16 and IC12) are	not been used.
RSTN Pin of IC13 connected to +3V3 to allow this chips work when AD9516 is reset.
6.- Power_Supply:
Diode D16 PN changed for S2M-TP
7.- RS232_and_USB_ports
Changed USB schematics ports for CPU_USB harness.
8.- FPGA_Peripherals_Control
Pin swapping updated in FPGA symbol.
Added signal CLK_EN to control IC12.

Footprints modified:
- Diode TS4148RZ: from CC1608-0603 to CD1608-0603
- MT29F4G16ABCHC NAND Flash, silkscreen increased from 9x11mm to 10,5x13mm
- FSM6JSMA switch footprint changed.
- Diode S2M footprint changed from DIOM5336X265N to DO-214AA/SMB-MCC.
- MT47H32M16HR DDR memory footprint changed.
- ARM JTAG HEADER footprint changed.

Routing:
- LDO_IN Polygon changed.
- Routing of C2 changed.
- Routing of R189, R186 and C265
SilkScreen:
- Top Layer:
  - Added OH Repository information
  - Added +5V connector polarity
- Bottom Layer:
  - Added license OHL information
  - Added version 3.1 of PCB
  - Added date