# PCB General data.
- Dimension: 439,06 mm x 174,40mm
- Thickness: 1,49 mm ± 10%
- Number of layers: 4
  - 2 routing layers (“Top Layer” and “Bottom Layer”)
  - 2 plane layers (“GND” and “PWR”)
- Components total: 480 (top: 156, bottom: 324)
- SMD components: Yes, both sides
- Silkscreen: Yes, both sides
- Nets: 434
- Vias: 1182
  - Hole Size: 0,3 mm
  - Via Diameter: 0,7 mm
- Pads: 2253
- Plating Finish: Nickel-Gold
- Controlled Impedance: Yes, on “Top Layer” and “Bottom Layer”
# Stack-Up Diagram
Top Layer				17 + 25 µm
PrePreg				178 µm
GND				35 µm
Core				980 µm
PWR				35 µm
PrePreg				178 µm
Bottom Layer				17 + 25 µm
Thickness Total:				1,49 mm ± 10%

# Layer Stack-Up Detail
Layer / Name	Gerber / Document	Copper / Thickness	Dielectric / Height	Dielectric / Material	Dielectric / Constant	50Ώ Impedance Width	100Ώ Differential Impedance Width/Gap
Top / Solder Mask	(.GTS)		0,010mm	Solder Resist	3,5
Top Layer	(.GTL)	0,042mm				0,3mm	0,2mm/0,2mm
PrePreg			0,178mm	FR-4	4,8
GND	(.GP1)	0,035mm
Core			0,98mm	FR-4	4,8
PWR	(.GP2)	0,035mm
PrePreg			0,178mm	FR-4	4,8
Bottom Layer	(.GBL)	0,042mm				0,3mm	0,2mm/0,2mm
Bottom / Solder Mask	(.GBS)		0,010mm	Solder Resist	3,5